## Slide 1: SDR Transceivers

## Slide 2: Disclaimer
Will not cover all transceivers
Not endorsing anything
Not endorsing anything

## Slide 3: GNURadio without Transceivers
What would GR today be without accessible transceivers?

## Slide 4
Approx. release of support for RTL dongle

## Slide 5: Evolution of moving samples
USB 2.0 – 8 MHz
1 Gig Ethernet – 25 MHz
PCIe (v2) – 100 Mhz per lane *
USB 3.0 – 125 MHz *
10 Gig Ethernet – 250 MHz *
Thunderbolt – 500 MHz *

## Slide 6: More Evolution!
2004
Basic TX/RX
Dec 2004
TVRX
March 05
DBSRX
June 05
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
2016
LFRX/TX + RFX
Mar 06
XCVR
Feb 09
BURX
Mar 10
WBX
Jan 10
SBX
Feb 11
RTL
Mar 12
PicoSDR
Feb 13
HackRF
Mar 13
UmTRX
Apr 13
CBX
Jun 13
BladeRF
Jul 13
B2XX
Aug13
SideKiq
May 14
E3XX
Nov 14
UBX
Feb 15
PocketSDR
Jun 15
0 MHz
6 GHz
3 GHz
1 GHz
2 GHz
4 GHz
5 GHz

## Slide 7: Transceivers w/ GNURadio Source/Sink Support
Ettus UHD Devices
B2XX
  Freq: 70 MHz – 6 GHz
  Resolution: 12-bit
  2 Channels
  USB 3.0
E3XX
  Freq: 70 MHz – 6 GHz
  Resolution: 12-bit
  2 Channels
  Embedded Xilinx Zynq
X3XX
  Freq: Daughtercard
  Resolution: 14-bit ADC, 16-bit DAC
  Bandwidth: 120 MHz
  2 Channels
  PCIex4, ExpressCard, or 10 GigE
N2XX
  Freq: Daughtercard
  Resolution: 14-bit ADC, 16-bit DAC
  Bandwidth: 25 MHz
  Gigabit Ethernet

## Slide 8: Transceivers w/ GNURadio Source/Sink Support
Ettus UHD Daughtercards
UBX
  Freq: 10 MHz – 6 GHz
  RF shielding
CBX
  Freq: 1.2 GHz – 6 GHz
SBX
  Freq: 400 MHz – 4.4 GHz
WBX
  Freq: 50 MHz – 2.2 GHz
  Granddaughter card
All have 120 MHz X-series options

## Slide 9: Transceivers w/ GNURadio Source/Sink Support
DRS PicoFlexor
Freq range:
  2 MHz – 3 GHz
  2 MHz – 12.4 GHz with option
Resolution: 8 bits
Dynamic Range: not provided
Instantaneous bandwidth: 6 or 25 MHz
Receive only
2 Channels
OMAP DM3730 onboard
USB 2.0
gr-dsp – OMAP DSP blocks for GNU Radio provided

## Slide 10: Transceivers w/ GNURadio Source/Sink Support
Epiq Sidekiq
Freq range: 70 MHz – 6 GHz
Resolution: 12-bit
Instantaneous bandwidth: 50 MHz
TX/RX full duplex
2 Channels – phase coherent
MiniPCIe x1 or USB 2.0

## Slide 11: Transceivers w/ GNURadio Source/Sink Support
RTL-SDR
Parameters vary depending on the part
Freq range: ~25 MHz – 2100 MHz
Resolution: 8 bits
Dynamic Range: not provided
Instantaneous bandwidth: 2.56 MHz
Receive only
USB 2.0

## Slide 12: Transceivers w/ GNURadio Source/Sink Support
UmTRX
  Freq range: 300 MHz – 3.8 GHz
  Resolution: 12-bit
  Instantaneous bandwidth: 13 MHz
  TX/RX full duplex
  2 Channels
  Gigabit Ethernet

## Slide 13: Kickstarted Transceivers
HackRF
  Freq range: 10 MHz – 6 GHz
  Resolution: 8-bit
  Instantaneous bandwidth: 8-20 MHz
  TX/RX half duplex
  2 Channels
  USB 2.0
$602,960

## Slide 14: Kickstarted Transceivers
BladeRF
  Freq range: 300 MHz – 3.8 GHz
  Resolution: 12-bit
  Instantaneous bandwidth: 28 MHz
  TX/RX full duplex
  2 Channels
  USB 3.0
$191,422

## Slide 15: Kickstarted Transceivers
PortableSDR – HF/Shortwave
  Freq range: 0 MHz – 35 MHz
  Instantaneous bandwidth: ? Hz
  ARM Processor - ARM Cortex-M4
  TX/RX full duplex
  GPS onboard
  Sweet color LCD screen
  USB 2.0
$66,197

## Slide 16: Four Channels!!
Ettus QuadRadio
  Freq range: 700 MHz – 4 GHz
  Resolution: 16-bit
  Instantaneous bandwidth: 60MHz
  1,2,3 or 4 RX Channels – Phase coherent
    “Stackable” up to 32-channels
  2 x 10 GigE

## Slide 17: Four Channels!!
SilverPalm SP-830X
  Freq range: 300 MHz – 4 GHz
  Resolution: 16-bit
  Instantaneous bandwidth: 20MHz
  TX/RX full duplex
  1,2,3 or 4 RX Channels and 1 TX
  USB 3.0, PCIe x2, 10GE,
  or Thunderbolt

## Slide 18: Four Channels!!
Nutaq PicoSDR
  Freq range: 300 MHz – 3.8 GHz
  Resolution: 12-bit
  Instantaneous bandwidth: 1.5 – 28 MHz
  TX/RX full duplex
  2 or 4 Channels
  1 GigE and/or PCIe x4

## Slide 19: Interfacing with GNURadio
gr-uhd
gr-osmocom
gr-baz
gr-sidekiq
RTL
USRPs
sidekiq
hackRF
bladeRF
UmTRX
Funcube
gr-dubri
DRS

## Slide 20: Questions?