&
Paul Cercueil
2015/08/26
(IIO blocks for GNU Radio)

---
The IIO Framework
- Industrial Input / Output framework (IIO)
  - All non human-interface I/O
- In the Linux kernel since 2.6.32 (2009), out of staging since 3.5 (2012)
- ~220 drivers (Linux 4.3)
  - ~70 drivers for ~400 ADI products
[Speaker Notes: analog-to-digital or digital-to-analog converters Precession ADCs / DACs high-speed ADCs / DACs Accelerometers, gyroscopes, IMUs Pressure, temperature and light sensors, etc.]

---
The IIO Framework
- Configuration interface
  - Special files in the Linux filesystem tree, with standardized filenames
  /sys/bus/iio/devices/iio:device0/name
  /sys/bus/iio/devices/iio:device0/out_voltage0_V1_raw
  /sys/bus/iio/devices/iio:device0/out_voltage0_V1_scale
  /sys/bus/iio/devices/iio:device0/out_voltage0_V1_powerdown
  /sys/bus/iio/devices/iio:device0/out_voltage0_V1_powerdown_mode
  /sys/bus/iio/devices/iio:device0/out_voltage1_V2_raw
  /sys/bus/iio/devices/iio:device0/out_voltage1_V2_scale
  /sys/bus/iio/devices/iio:device0/out_voltage1_V2_powerdown
  /sys/bus/iio/devices/iio:device0/out_voltage1_V2_powerdown_mode

---
The IIO Framework
- Buffer interface
  - For reading and writing samples
    /dev/iio:device0
    /dev/iio:device1
    …
  - Two possible uses:
    - Standard I/O calls (read / write)
    - Faster mmap based interface (not yet upstream)

---
Libiio
- https://github.com/analogdevicesinc/libiio.git
- Software library to interface the IIO framework
- Written in C, licensed under LGPL v2.1+
- Has bindings: Python, C#, C++, MATLAB, Simulink
- Abstracts away the low-level details of the kernel ABI
[Speaker Notes: Problem was : every client rewrites the same low-level code Young project (1 year old)]

---
Libiio
- Four objects:
  - iio_context
  - iio_device
  - iio_channel
  - iio_buffer
- Attributes (C strings)

---
Modularity
- Libiio is designed with two different layers.
  - One high-level layer (API functions and objects)
  - Interchangeable backends:
    - Local backend
    - Network backend
    - TODO : USB, PCIe backends
- One application using libiio will work the same independently of the backend used.

---
Local backend
- When running on the target board. The IIO devices reported by the Linux kernel are used.
- Only available for Linux (obviously).
- Limitations:
  - No concurrent access
  - Requires super-user rights

---
Network backend
- Connects to a server running on the target
- Cross-platform (UNIX, OSX, Windows…)
- More secure (applications don't need super-user rights)
- The server handles concurrent access, and multiplexing / demultiplexing sample streams.

---
IIOD

---
Applications and tools
- iio_info
  - Displays information about the IIO context
- iio_readdev
  - Capture data from a IIO device
# iio_info
Library version: 0.5 (git tag: 58c9c84)
IIO context created with network backend.
Backend version: 0.5 (git tag: 2272450)
Backend description string: 10.44.2.209 Linux analog 4.0.0-07433-g4d355a2 #452 SMP PREEMPT Wed Aug 19 11:44:53 CEST 2015 armv7l
IIO context has 5 devices:
    iio:device0: ad7291
        9 channels found:
        temp0: (input)
        3 channel-specific attributes found:
        attr 0: scale value: 250
        attr 1: mean_raw value: 100
        attr 2: raw value: 99
        voltage0: (input)
        2 channel-specific attributes found:
        attr 0: raw value: 3342
        attr 1: scale value: 0.610351562
        voltage1: (input)
        2 channel-specific attributes found:
        attr 0: raw value: 3359
        attr 1: scale value: 0.610351562

---
IIO blocks for GNU Radio: gr-iio
- https://github.com/analogdevicesinc/gnuradio.git
- Our usecase:
  - GR is an analytics tool for RF impairments
  - ADI customers want to use GNU Radio on their custom boards
- If you need radio peripheral, use B210, Sidekiq, AgileSDR, etc.

---
IIO blocks for GNU Radio: gr-iio
- Impossible… until now
  - GNU Radio is too heavy for development boards
  - Solution : use Libiio, stream the samples!
- The IIO blocks are just a tiny wrapper around libiio
  - ~200 lines of C++

---
IIO blocks for GNU Radio: gr-iio
- Generic sink and source blocks
  - Work with every converter supported by the IIO framework
  - Not limited to high-speed converters…

---
IIO blocks for GNU Radio: gr-iio

---
IIO blocks for GNU Radio: gr-iio
- FMCOMMS-2/3/4/5 blocks
  - Tiny wrappers around the generic blocks
  - For ADI's reference designs

---
Performance
- ~18 MSPS for one I/Q 16-bit channel (480 Mbit/s)
- CPU or network limited
- Future improvements:
  - Zero-copy (IIO device to network without copying the data)
  - USB3, PCIe backends